## Slide 1
Codex Verification Agent
for RTL Testbench Generation
Mini Project 2 - Phase 2 | AI for Design Verification
Topic 2: Agent pipeline with prompt engineering for automated hardware verification
Codex CLI / gpt-5.4
iverilog / vvp
Python Agent
ICLAD Benchmark
1

## Slide 2
Problem Definition
2
The ICLAD Verification Task
Each problem: one specification.md + 31 candidate RTL implementations (mutant_*.v).
Only one implementation is correct; the rest have injected bugs.
Agent must generate a self-checking Verilog testbench that passes only the correct design.
Scoring Metric
Score = 1 / (# passing implementations)
Ideal: exactly 1 of 31 passes -> Score = 1.0
Discrimination Goal
specification.md
Verification Agent
testbench.v -> score: 1.0
mutant_0.v correct
mutant_1.v bug
mutant_2.v bug
... (31 total)
2

## Slide 3
Agent Architecture
3
specification.md
parse_spec.txt
parsed_spec.json
gen_testplan.txt
test_plan.json
spec.md + parsed_spec
+ test_plan
gen_testbench.txt
(or gen_testbench_protocol.txt
if FIFO / CDC / credit module)
tb/<name>_tb.v
iverilog + vvp simulation
if compile fails
repair_testbench.txt
Input file
Prompt (.txt)
Structured output (.json)
Generated Verilog (.v)
Repair path
Repair if compile fails * Refine if score < 1.0 * Rescue refinement if all mutants fail
3

## Slide 4
Prompt Engineering Strategy - The Core Contribution
4
The key insight: don't just generate valid Verilog - generate a trustworthy oracle.
1. Structured Spec Parsing
Parser forces Codex to separate:
* guaranteed_properties
* ambiguous_properties
* forbidden_assumptions
Foundation for safe oracle generation.
2. Oracle-Style Selection
Each problem routed to one of:
* formula - combinational mappings
* cycle_accurate - simple sequential
* protocol_invariant - FIFO/CDC/credit
Prevents overconfident assertions.
3. Safe vs. Unsafe Checks
Test plan explicitly produces:
* safe_checks - grounded assertions
* unsafe_checks - avoid these
Stops testbench from rejecting the
correct implementation by accident.
4. Protocol-Specific Prompting
Dedicated prompt (gen_testbench_protocol.txt) instructs Codex to avoid: exact CDC latency, exact counter arithmetic, exact queue-depth equalities, bounded credit-pulse windows unless the spec explicitly guarantees them.
5. Repair-Mode & Guardrail Regen
repair_testbench.txt is separate from generation - keeps compile fixes focused on simplifying an over-strong oracle. Guardrail check screens for unsafe bounded-wait patterns before simulation; triggers regeneration if found.
Impact: counter went from failing to score = 1.0 after ambiguity-aware prompt refinement.
4

## Slide 5
Results
5
10 visible benchmark problems evaluated * Average score: 0.7 * 1 iteration each, 31 mutants per problem
Problem
Type
Passing
Score
Compile
Errors
Oracle
Mode
Outcome
ecc_sed_encoder
Comb.
1/31
1.0000
0
formula
Score = 1.0
enc_bin2gray
Comb.
1/31
1.0000
0
formula
Score = 1.0
enc_bin2onehot
Comb.
1/31
1.0000
0
formula
Score = 1.0
lfsr
Seq.
1/31
1.0000
0
cycle-acc.
Score = 1.0
shift_left
Comb.
1/31
1.0000
0
formula
Score = 1.0
shift_right
Comb.
1/31
1.0000
0
formula
Score = 1.0
counter
Seq.
1/31
1.0000
0
cycle-acc.
Score = 1.0
credit_receiver
Proto.
0/31
0.0000
0
proto_inv.
Oracle failure
fifo_flops
Proto.
0/31
0.0000
0
proto_inv.
Oracle failure
cdc_fifo_flops_push_credit
Proto.
0/31
0.0000
0
proto_inv.
Oracle failure
7 / 10
Problems Solved
(Score = 1.0)
0
Compile Failures
on solved set
0.7
Average Score
across all 10
3
Protocol Cases
Still Open
5

## Slide 6
What Worked, What's Hard & Next Steps
6
What Worked
Strong on formula / cycle-accurate
7/10 visible problems -> score = 1.0 with zero compile failures
counter recovered via prompt fix
Ambiguity-aware parsing turned a formerly failing case to 1/31
Full artifact trail
Parsed spec JSON, test plan, sim logs - fully reproducible
Compile stability improved
Guardrail regen + repair prompt eliminated compile errors on solved set
The Hard Problem
Protocol oracle generation
FIFO / CDC / credit modules: Codex invents exact latency, counter, or queue-depth assumptions not in the spec
Over-confident assertions
Generated oracle rejects even the correct mutant because spec timing is ambiguous
Spec ambiguity not tool errors
Remaining 3 failures are not syntax - they are semantic oracle failures
Not a solvable shortcut
Cannot hardcode reference checkers - must remain professor-safe / Codex-driven
Phase 3 Plan
Full visible benchmark run
Report aggregate metrics across complete ICLAD visible set
Stronger protocol prompting
Push oracle_style: protocol_invariant further; test interface-only assertions
Repair loop for oracle mismatches
Not just compile repair - also detect all-fail and soften oracle
Deterministic post-processing
Rule-based rewriter to remove overly specific invariants before simulation
Takeaway: 7/10 solved cleanly. The remaining challenge is semantic - constructing a trustworthy oracle from ambiguous protocol specs.
6