## Slide 1
Arizona State University
Codex Verification Agent
for RTL Testbench Generation
Mini Project 2 - Phase 3 | GenAI for Design Verification | Topic 2
Agent pipeline with prompt engineering for automated hardware verification
Phase 3 Submission
9 / 10
Problems Solved
1 / 31
Ideal Score
0
Compile Failures
1

## Slide 2
Problem Definition
2
The ICLAD Verification Task
Each problem: one specification.md + 31 candidate RTL implementations (mutant_*.v).
Only one implementation is correct; the rest have injected bugs.
Agent must generate a self-checking Verilog testbench that passes only the correct design.
Scoring Metric
Score = 1 / (# passing implementations)
Ideal: exactly 1 of 31 passes -> Score = 1.0
Discrimination Goal
specification.md
Verification Agent
testbench.v -> score: 1.0
mutant_0.v correct
mutant_1.v bug
mutant_2.v bug
... (31 total)
2

## Slide 3
Agent Architecture
3
Parse
Spec
NL → JSON +
oracle fields
Build
Test Plan
safe / unsafe
checks
Generate
TB
route: general
or protocol
Guardrail
Check
reject unsafe
patterns
Simulate
+ Score
iverilog/vvp
all mutants
Repair: if compile fails · Refine: if score < 1.0 (rescue refinement on total failure)
Key Components
agent.py
Full orchestration: parse → plan → generate → guardrail → simulate → repair/refine
spec_parser.py
Extracts oracle_style, guaranteed_properties, ambiguous_properties, forbidden_assumptions
tb_generator.py
Routes to general or protocol prompt; applies deterministic post-processing
simulator.py
iverilog -g2012 compilation + vvp simulation across all mutants
run_pipeline.py
Single-command entry point for end-to-end execution
Agent vs. One-Shot Prompt
Intermediate Artifacts
Parsed spec JSON + test plan saved and reused across steps
Real Tool Invocation
Calls iverilog/vvp, reads stdout/stderr, parses PASS/FAIL
Execution Feedback
Compile errors and scores fed back for repair and refinement
Guardrail-Driven Regen
Protocol testbenches structurally screened before simulation
3

## Slide 4
Agent Architecture
3
specification.md
parse_spec.txt
parsed_spec.json
gen_testplan.txt
test_plan.json
spec.md + parsed_spec
+ test_plan
gen_testbench.txt
(or gen_testbench_protocol.txt
if FIFO / CDC / credit module)
tb/<name>_tb.v
iverilog + vvp simulation
if compile fails
repair_testbench.txt
Input file
Prompt (.txt)
Structured output (.json)
Generated Verilog (.v)
Repair path
Repair if compile fails * Refine if score < 1.0 * Rescue refinement if all mutants fail
3

## Slide 5
Prompt Engineering Strategy - The Core Contribution
4
The key insight: don't just generate valid Verilog - generate a trustworthy oracle.
1. Structured Spec Parsing
Parser forces Codex to separate:
* guaranteed_properties
* ambiguous_properties
* forbidden_assumptions
Foundation for safe oracle generation.
2. Oracle-Style Selection
Each problem routed to one of:
* formula - combinational mappings
* cycle_accurate - simple sequential
* protocol_invariant - FIFO/CDC/credit
Prevents overconfident assertions.
3. Safe vs. Unsafe Checks
Test plan explicitly produces:
* safe_checks - grounded assertions
* unsafe_checks - avoid these
Stops testbench from rejecting the
correct implementation by accident.
4. Protocol-Specific Prompting
Dedicated prompt (gen_testbench_protocol.txt) instructs Codex to avoid: exact CDC latency, exact counter arithmetic, exact queue-depth equalities, bounded credit-pulse windows unless the spec explicitly guarantees them.
5. Repair-Mode & Guardrail Regen
repair_testbench.txt is separate from generation - keeps compile fixes focused on simplifying an over-strong oracle. Guardrail check screens for unsafe bounded-wait patterns before simulation; triggers regeneration if found.
Impact: counter went from failing to score = 1.0 after ambiguity-aware prompt refinement.
4

## Slide 6
Results
5
10 visible benchmark problems evaluated * Average score: 0.9 * 1 iteration each, 31 mutants per problem
Problem
Type
Passing
Score
Compile
Errors
Oracle
Mode
Outcome / Correct Mutant
ecc_sed_encoder
Comb.
1/31
1.0
0
formula
mutant_18
enc_bin2gray
Comb.
1/31
1.0
0
formula
mutant_25
enc_bin2onehot
Comb.
1/31
1.0
0
formula
mutant_27
lfsr
Seq.
1/31
1.0
0
cycle-acc.
mutant_29
shift_left
Comb.
1/31
1.0
0
formula
mutant_1
shift_right
Comb.
1/31
1.0
0
formula
mutant_9
counter
Seq.
1/31
1.0
0
cycle-acc.
mutant_11
credit_receiver
Proto.
1/31
1.0
0
proto_inv.
mutant_18
fifo_flops
Proto.
1/31
1.0
0
proto_inv.
mutant_23
cdc_fifo_flops_push_credit
Proto.
0/31
0.0
0
proto_inv.
-- Oracle failure --
9 / 10
Problems Solved
(Score = 1.0)
0
Compile Failures
on solved set
0.9
Average Score
across all 10
1
Protocol Cases
Still Open
5

## Slide 7
What Worked, What's Hard & Phase 3 Outcomes
6
What Worked
9/10 solved cleanly
Formula, cycle-accurate, AND protocol modules (credit_receiver, fifo_flops) now score 1.0
counter recovered via prompt fix
Ambiguity-aware parsing turned a formerly failing case to 1/31
Full artifact trail
Parsed spec JSON, test plan, sim logs - fully reproducible
Compile stability
Guardrail regen + repair prompt - zero compile errors across entire solved set
The Hard Problem
cdc_fifo_flops_push_credit
Spec is extremely large; context size causes LLM timeout. Oracle rejects all 31 including correct.
Over-confident timing assertions
Codex invents exact synchronization latency not guaranteed by spec
Spec ambiguity
Remaining failure is semantic oracle failure, not a syntax or tool error
Not a solvable shortcut
Cannot hardcode reference checkers - must remain Codex-driven
Phase 3 Outcomes
Full visible benchmark run
All 10 problems evaluated - 9/10 score 1.0, aggregate metrics reported
Protocol module breakthrough
credit_receiver and fifo_flops now solved via stronger protocol-invariant prompting
Repair + rescue flow validated
All-fail rescue refinement confirmed working across sequential modules
One remaining open problem
cdc_fifo_flops_push_credit: context-size + timing ambiguity - future property synthesis target
Takeaway: 9/10 solved cleanly including protocol modules. One CDC case remains open due to context-window limits and semantic ambiguity.
6